## Slide 1: Chapter 5: Machine Dependent Optimizations
Topics
  Machine-Dependent Optimizations
    Pointer code
    Unrolling
    Enabling instruction level parallelism
  Understanding Processor Operation
    Translation of instructions into operations
    Out-of-order execution of operations
  Limits on Optimization
  Profiling Tools

## Slide 2: Announcements
Attack Lab #3 grading during this week
Floating point recitation exercise due Monday
Performance recitation exercise released later this, due in about a week
Performance Lab #4 available, due Friday November 8
  Optimize code to improve performance
Read:
  Chapter 5
  Do practice problems

## Slide 3: Machine-Dependent Optimizations
Take advantage of some knowledge of the hardware organization of the CPU to squeeze faster performance from the executing program
  Exploit the pipelining within the CPU
  Exploit the parallelism within the CPU
    There may be multiple units that perform addition, multiplication, etc.
    Multiple instructions can execute in parallel on different units
    This is called instruction-level parallelism

## Slide 4: Modern CPU Design
Execution Unit (EU)
Functional
Units
Integer/
Branch
FP
Add
FP
Mult/Div
Load
Store
Data
Cache
Data
Data
Addr.
Addr.
General
Integer
Operation Results
Instruction Control Unit (ICU)
Instruction
Cache
Fetch
Control
Instruction
Decode
Address
Instrs.
Operations
Prediction
OK?
Retirement
Unit
Register
File
Register
Updates
Extends Y86 Design with multiple Functional Units in a Pentium P6
  1 load
  1 store
  2 integer (one may be branch)
  1 FP Addition
  1 FP Multiplication or Division

## Slide 5: Parallel Execution across Functional Units
Execution Unit (EU)
Functional
Units
Instruction Control Unit (ICU)
Integer/
Branch
FP
Add
FP
Mult/Div
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instrs.
Operations
Prediction
OK?
Data
Data
Addr.
Addr.
General
Integer
Operation Results
Retirement
Unit
Register
File
Register
Updates
Code Example:
  addl %eax, %ebx
  sall $4, %esi
  fmul …
  fadd …
  cmpl %ecx, %edx
  jle …
addl
fmul
fadd
cmpl
  Instructions can run at the same time in parallel on different functional units
    This is called instruction-level parallelism
  Instruction re-ordering may occur
    In this example, fmul and fadd can execute before sall if independent

## Slide 6: Pipelined Execution Within Functional Units
Each Individual Functional Unit may be pipelined
Example: Integer Multiply
  Delay = 4 cycles, but
  Throughput = 1 instruction/cycle, i.e. can issue a new instruction to it every 1 cycle, i.e. Issue time = 1 cycle
    This is because of multiple stages of pipelining internal to the Integer Multiply unit

## Slide 7: Pipelined Execution Within Functional Units
Capabilities of a Pentium P6 CPU:
  Instruction Latency Cycles/Issue
  Integer Add 1 0.5
  Load / Store 3 1
  Integer Multiply 4 1
  Integer Divide 36 36
  Double/Single FP Multiply 5 2
  Double/Single FP Add 3 1
  Double/Single FP Divide 38 38
Notes: The reason the Cycles/Issue is less than one (=0.5) is because there are two integer units.

## Slide 8: Pipelined Execution Within Functional Units
Capabilities of an Intel Core i7:
Notes: The reason the Cycles/Issue is less than one (=0.33) is because there are three integer units.
“the latencies and issue times for division are given as ranges, because some combinations of dividend and divisor require more steps than others.” p. 501 of 2nd ed

## Slide 9: Pipelined Execution
Execution Unit (EU)
Functional
Units
Instruction Control Unit (ICU)
Integer/
Branch
FP
Add
FP
Mult/Div
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instrs.
Operations
Prediction
OK?
Data
Data
Addr.
Addr.
General
Integer
Operation Results
Retirement
Unit
Register
File
Register
Updates
Code Example:
  ...
  imull %eax, %ebx
  immul %ecx, %edx
  immul %edi, %esi
  ...
  All 3 instructions can be pipelined in an integer multiply at different stages of execution
Generally, can mix both parallel and pipelined execution inside CPU

## Slide 10: Instruction Control
Grabs Instruction Bytes From Memory
  Based on current PC + predicted targets for predicted branches
  Hardware dynamically guesses whether branches taken/not taken and (possibly) branch target
Translates Instructions Into Operations
  Primitive steps required to perform instruction
  Typical instruction requires 1–3 operations
Converts Register References Into Tags
  Abstract identifier linking destination of one operation with sources of later operations
Instruction Control
Instruction
Cache
Fetch
Control
Instruction
Decode
Address
Instrs.
Operations
Retirement
Unit
Register
File

## Slide 11: Previous Best Combining Code
void combine4(vec_ptr v, int *dest)
{
int i;
int length = vec_length(v);
int *data = get_vec_start(v);
int sum = 0;
for (i = 0; i < length; i++)
sum += data[i];
*dest = sum;
}
combine1
combine2
combine3
combine4

## Slide 12: Translation Example
Version of Combine4
  Integer data, add operation
.L24: # Loop:
addl (%eax,%edx,4),%ecx # sum += data[i]
incl %edx # i++
cmpl %esi,%edx # i:length
jl .L24 # if < goto Loop
.L24:
addl (%eax,%edx,4),%ecx
incl %edx
cmpl %esi,%edx
jl .L24
load (%eax,%edx.0,4)  t.1
iaddl t.1, %ecx.0  %ecx.1
incl %edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1
Translation of First Iteration
  ICU fetches add instruction & translates it to 2 operations for functional units, 1 for the load unit, 1 for an integer unit

## Slide 13: Visualizing Operations
Data-flow graph
  load’s latency = 3 clock cycles, but can be pipelined
  add’s latency = 1 clock cycle
Time
cc.1
t.1
%ecx.i +1
incl
cmpl
jl
load
%edx.0
%edx.1
%ecx.0
addl
%ecx.1
load
load (%eax,%edx.0,4)  t.1
iaddl t.1, %ecx.0  %ecx.1
incl %edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1
Operations
  Note add depends on load completing first, but inc, cmp and jl are independent, so can execute in parallel!
  We see register renaming inside the functional units, e.g. %edx.1 (see text)
    Many instructions are spread over different functional units and are operating on different versions of registers

## Slide 14: 4 Iterations of Combining Sum
Unlimited Resource Analysis, e.g. at least 4 loads & 4 integer units
Performance
  Can begin a new iteration on each clock cycle
  Should give CPE of 1.0
  Would require executing 4 integer operations in parallel
4 integer ops

## Slide 15: Combining Sum: Resource Constraints
  Only have two integer functional units
  One pipelined load unit
  Some operations delayed even though operands available
  Set priority based on program order
Performance
  Delay = 4-5 cycles, but CPE = 2.0

## Slide 16: Translation Example
Version of Combine4
  Integer data, multiply operation
Translation of First Iteration
.L24: # Loop:
imull (%eax,%edx,4),%ecx # t *= data[i]
incl %edx # i++
cmpl %esi,%edx # i:length
jl .L24 # if < goto Loop
.L24:
imull (%eax,%edx,4),%ecx
incl %edx
cmpl %esi,%edx
jl .L24
load (%eax,%edx.0,4)  t.1
imull t.1, %ecx.0  %ecx.1
incl %edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1

## Slide 17: Visualizing Operations
Operations
  Vertical position denotes time at which executed
    Cannot begin operation until operands available
  Height denotes latency, so imull takes 4 clock cycles
Operands
  Arcs shown only for operands that are passed within execution unit
cc.1
t.1
load
%ecx.1
incl
cmpl
jl
%edx.0
%edx.1
%ecx.0
imull
load (%eax,%edx,4)  t.1
imull t.1, %ecx.0  %ecx.1
incl %edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1
Time

## Slide 18: 3 Iterations of Combining Product
Unlimited Resource Analysis
Performance
  Can’t use imull pipeline due to data dependency
  Limiting factor becomes latency of integer multiplier
  Gives CPE of 4.0
  Even with infinite # of integer units, cannot do better than this
Notes: Even though the imull integer multiplier can be pipelined, we are unable to take advantage of the pipeline, because of the dependency of the data between iteration, i.e. for iteration i, %ecx.i+1 depends on the imull using %ecx.i to finish.

## Slide 19: Loop Unrolling
Optimization
  Combine multiple iterations into single loop body
  Amortizes loop overhead across multiple iterations
  Finish extras at end
  Measured CPE = 1.33
  This is a machine-dependent optimization
void combine5(vec_ptr v, int *dest)
{
int length = vec_length(v);
int limit = length-2;
int *data = get_vec_start(v);
int sum = 0;
int i;
/* Combine 3 elements at a time */
for (i = 0; i < limit; i+=3) {
sum += data[i] + data[i+1]
+ data[i+2];
}
/* Finish any remaining elements */
for (; i < length; i++) {
sum += data[i];
}
*dest = sum;
}

## Slide 20: Visualizing Unrolled Loop
  Loads can pipeline, since don’t have dependencies
  Only one set of loop control operations
load (%eax,%edx.0,4)  t.1a
iaddl t.1a, %ecx.0c  %ecx.1a
load 4(%eax,%edx.0,4)  t.1b
iaddl t.1b, %ecx.1a  %ecx.1b
load 8(%eax,%edx.0,4)  t.1c
iaddl t.1c, %ecx.1b  %ecx.1c
iaddl $3,%edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1
Time
%edx.0
%edx.1
%ecx.0c
cc.1
t.1a
%ecx.i +1
addl
cmpl
jl
addl
%ecx.1c
addl
addl
t.1b
t.1c
%ecx.1a
%ecx.1b
load
load
load

## Slide 21: Executing with Loop Unrolling
  Predicted Performance
    CPE = 1.0. One iteration in 3 cycles, and 3 elements per iteration
    Loop unrolling allowed add/cmp/jl to be shifted in time so as not to conflict with the add after the load, (only 2 int units)
  Measured Performance
    CPE of 1.33, One iteration every 4 cycles
Notes: The discrepancy between predicted and actual measured performance may be due to our model of the hardware being imperfect.

## Slide 22: Effect of Unrolling
  Only helps integer sum for our examples
    Other cases constrained by functional unit latencies
  Effect is nonlinear with degree of unrolling
    Many subtle effects determine exact scheduling of operations
Unrolling Degree |  | 1 | 2 | 3 | 4 | 8 | 16
Integer | Sum | 2.00 | 1.50 | 1.33 | 1.50 | 1.25 | 1.06
Integer | Product | 4.00 |  |  |  |  | 
FP | Sum | 3.00 |  |  |  |  | 
FP | Product | 5.00 |  |  |  |  | 

## Slide 23: Visualizing Parallelism
data[i]
data[i+1]
data[i+2]
data[i+3]
data[i+4]
data[i+5]
data[i+6]
data[i+7]
data[i+8]
data[i+9]
data[i+10]
data[i+11]
data[i+12]
data[i+13]
data[i+14]
combine5...{
...
for (i = 0; i < limit; i+=3) {
sum += data[i] + data[i+1]
+ data[i+2];
}
...
}
Loop unrolling with k=3
combine6...{
...
for (i = 0; i < limit; i+=3) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+1];
acc2 = acc2 + data[i+2];
}
sum = acc0 + acc1 + acc2;
...
}
Loop unrolling with k=3, and
Parallel accumulators
…
…

## Slide 24: Visualizing Parallelism (2)
…
…
data[i]
data[i+1]
data[i+2]
data[i+3]
data[i+4]
data[i+5]
data[i+6]
data[i+7]
data[i+8]
data[i+9]
data[i+10]
data[i+11]
data[i+12]
data[i+13]
data[i+14]
combine6...{
...
for (i = 0; i < limit; i+=3) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+1];
acc2 = acc2 + data[i+2];
}
sum = acc0 + acc1 + acc2;
...
}
Loop unrolling with k=3, and
Parallel accumulators
acc0
acc1
acc2
  Each accumulator is independent of the other accumulators, so summing can occur in parallel
  Sum together accumulators at the last step

## Slide 25: Parallel Loop Unrolling
Code Version
  Integer product
Optimization
  Accumulate in two different products
    Can be performed simultaneously
  Combine at end
Performance
  CPE = 2.0
  2X performance
void combine6(vec_ptr v, int *dest)
{
int length = vec_length(v);
int limit = length-1;
int *data = get_vec_start(v);
int x0 = 1;
int x1 = 1;
int i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x0 *= data[i];
x1 *= data[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x0 *= data[i];
}
*dest = x0 * x1;
}

## Slide 26: Serial Product Computation
Computation
  ((((((((((((1 * x0) * x1) * x2) * x3) * x4) * x5) * x6) * x7) * x8) * x9) * x10) * x11)
*
*
1
x0
x1
*
x2
*
x3
*
x4
*
x5
*
x6
*
x7
*
x8
*
x9
*
x10
*
x11
int x=1; int i;
for (i = 0; i < limit; i++) {
x *= data[i];
}
Performance
  N elements, D cycles/operation
  N*D cycles

## Slide 27: Dual Parallel Product Computation
Computation
  ((((((1 * x0) * x2) * x4) * x6) * x8) * x10)
  *((((((1 * x1) * x3) * x5) * x7) * x9) * x11)
*
*
1
x1
x3
*
x5
*
x7
*
x9
*
x11
*
*
*
1
x0
x2
*
x4
*
x6
*
x8
*
x10
int x0 = 1; int x1 = 1; int i,x;
for (i = 0; i < limit; i+=2) {
x0 *= data[i];
x1 *= data[i+1];
}
...
x = x0 * x1;
Performance
  N elements, D cycles/operation
  (N/2+1)*D cycles
  ~2X performance improvement

## Slide 28: Visualizing Parallel Loop
  Two multiplies within loop no longer have data dependency
  Allows them to pipeline (issue time of integer multiply is 1 clock cycle)
load (%eax,%edx.0,4)  t.1a
imull t.1a, %ecx.0  %ecx.1
load 4(%eax,%edx.0,4)  t.1b
imull t.1b, %ebx.0  %ebx.1
iaddl $2,%edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1
...
for (i = 0; i < limit; i+=2) {
x0 *= data[i];
x1 *= data[i+1];
}
...
*dest = x0 * x1;
Time
%edx.1
%ecx.0
%ebx.0
cc.1
t.1a
imull
%ecx.1
addl
cmpl
jl
%edx.0
imull
%ebx.1
t.1b
load
load

## Slide 29: Executing with Parallel Loop
  Predicted Performance
    Can keep 4-cycle multiplier busy performing two simultaneous multiplications
    Gives CPE of 2.0
Notes: The loads may be drawn incorrectly. They should be shifted down more at each iteration to allow pipelining of the one load unit. As drawn, this would suggest there are at least 3 load units, e.g. look at row 3. Also, as drawn, the add/cmp/jl execution stream suggest overlap of at leas three integer units. But the point of this slide is not to focus on the loads and add/cmp/jl, but on the pipelined overlap of the multipliers enabled by having independent multiply streams (in this case, of even and odd elements of the data array).

## Slide 30: Requirements for Parallel Computation
Mathematical
  Combining operation must be associative & commutative
    OK for integer multiplication and addition
    Not strictly true for floating point
      We saw some pathological cases in the textbook where the order of floating point multiplication can cause overflow
        e.g. in Ch 2, for single precision floating point, “(1e20*1e20)*1e-20 evaluates to +∞, while 1e20*(1e20*1e-20) evaluates to 1e20.”
      OK for most applications
Hardware
  Pipelined functional units
  Ability to dynamically extract parallelism from code

## Slide 31: Optimization Results for Combining

## Slide 32: Parallel Unrolling: Reassociation
Code Version
  Integer product
Optimization
  Multiply pairs of elements together
  And then update product
  “Tree height reduction”
Performance
  CPE = 2.5
void combine6aa(vec_ptr v, int *dest)
{
int length = vec_length(v);
int limit = length-1;
int *data = get_vec_start(v);
int x = 1;
int i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x *= (data[i] * data[i+1]);
}
/* Finish any remaining elements */
for (; i < length; i++) {
x *= data[i];
}
*dest = x;
}

## Slide 33: Understanding Parallelism
  CPE = 4.00
  All multiplies performed in sequence and depend on the previous multiply
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = (x * data[i]) * data[i+1];
}
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = x * (data[i] * data[i+1]);
}
  CPE = 2.50
  Multiplies overlap: data[i]*data[i+1] independent of accumulator multiplies and next iteration multiply data[i+2]*data[i+3]

## Slide 34: Reassociation (Method #2) Computation
Computation
  ((((((1 * (x0 * x1)) * (x2 * x3)) * (x4 * x5)) * (x6 * x7)) * (x8 * x9)) * (x10 * x11))
Performance
  N elements, D cycles/operation
  Should be (N/2+1)*D cycles
    CPE = 2.0
  Measured CPE worse
*
*
1
*
*
*
*
*
x1
x0
*
x3
x2
*
x5
x4
*
x7
x6
*
x9
x8
*
x11
x10
Unrolling | CPE (measured) | CPE (theoretical)
2 | 2.50 | 2.00
3 | 1.67 | 1.33
4 | 1.50 | 1.00
6 | 1.78 | 1.00

## Slide 35: Summary: Results for Pentium III
  Biggest gain doing basic optimizations
  But, last little bit helps

## Slide 36: Figure 5.16 – Alternative Visualization

## Slide 37: Figure 5.18 - Alternative Visualization
Notes: This timing diagram is an alternative way to visualize the computation in each loop iteration, which helps identify bottlenecks/dependencies in the computations (see next slide).

## Slide 38: Figure 5.19 - Alternative Visualization

## Slide 39: Limitations of Parallel Execution
We saw in the previous slide that parallelizing to 8x8 actually resulted in worse performance
Need Lots of Registers
  e.g. to hold 8 parallel sums/products
  Only 6 usable integer registers on 32-bit systems
    Also needed for pointers, loop conditions
  8 FP registers on 32-bit systems
  When not enough registers, must spill temporaries onto stack
    Wipes out any performance gains
  Not helped by renaming
    Cannot reference more operands than instruction set allows
    Major drawback of IA32 instruction set

## Slide 40: Register Spilling Example
Example
  8 X 8 integer product, so 8 parallel accumulators for partial products
  7 local variables share 1 register
  See that we are storing locals on stack
    e.g., at -8(%ebp)
  All this memory manipulation essentially negates any performance gain due to parallelism
.L165:
imull (%eax),%ecx
movl -4(%ebp),%edi
imull 4(%eax),%edi
movl %edi,-4(%ebp)
movl -8(%ebp),%edi
imull 8(%eax),%edi
movl %edi,-8(%ebp)
movl -12(%ebp),%edi
imull 12(%eax),%edi
movl %edi,-12(%ebp)
  …
addl $32,%eax
addl $8,%edx
cmpl -32(%ebp),%edx
jl .L165
Notes: This is incomplete code, so it’s not clear why %ecx is at the top of the code.

## Slide 41: What About Branches?
Challenge
  Instruction Control Unit must work well ahead of Exec. Unit
    To generate enough operations to keep EU busy
80489f3: movl $0x1,%ecx
80489f8: xorl %edx,%edx
80489fa: cmpl %esi,%edx
80489fc: jnl 8048a25
80489fe: movl %esi,%esi
8048a00: imull (%eax,%edx,4),%ecx
Executing
Fetching &
Decoding
  When ICU encounters conditional branch, cannot reliably determine where to continue fetching
Notes: Loops conditionally branch, so we’re speculatively executing way ahead. For example, the ICU could be multiple loop indices in advance, and if a branch is incorrect, then we have to wait to refill the pipeline.

## Slide 42: Branch Outcomes
  When encounter conditional branch, cannot determine where to continue fetching
    Branch Taken: Transfer control to branch target
    Branch Not-Taken: Continue with next instruction in sequence
  Cannot resolve until outcome determined by branch/integer unit
80489f3: movl $0x1,%ecx
80489f8: xorl %edx,%edx
80489fa: cmpl %esi,%edx
80489fc: jnl 8048a25
80489fe: movl %esi,%esi
8048a00: imull (%eax,%edx,4),%ecx
Branch Not-Taken
8048a25: cmpl %edi,%edx
8048a27: jl 8048a20
8048a29: movl 0xc(%ebp),%eax
8048a2c: leal 0xffffffe8(%ebp),%esp
8048a2f: movl %ecx,(%eax)
Branch Taken

## Slide 43: Branch Prediction
Idea
  Guess which way branch will go
  Begin executing instructions at predicted position
    But don’t actually modify register or memory data
80489f3: movl $0x1,%ecx
80489f8: xorl %edx,%edx
80489fa: cmpl %esi,%edx
80489fc: jnl 8048a25
. . .
8048a25: cmpl %edi,%edx
8048a27: jl 8048a20
8048a29: movl 0xc(%ebp),%eax
8048a2c: leal 0xffffffe8(%ebp),%esp
8048a2f: movl %ecx,(%eax)
Predict Taken
Execute

## Slide 44: Branch Prediction Through Loop
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
i = 101
Assume vector length = 100
Read invalid location
Executed
Fetched

## Slide 45: Branch Misprediction Invalidation
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken (Oops)
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
i = 101
Invalidate
Assume vector length = 100

## Slide 46: Branch Misprediction Recovery
Performance Cost
  Misprediction on Pentium III wastes ~14 clock cycles
  That’s a lot of time on a high performance processor
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
80488b1: movl (%ecx,%edx,4),%eax
80488b4: addl %eax,(%edi)
80488b6: incl %edx
80488b7: cmpl %esi,%edx
80488b9: jl 80488b1
80488bb: leal 0xffffffe8(%ebp),%esp
80488be: popl %ebx
80488bf: popl %esi
80488c0: popl %edi
i = 98
i = 99
Predict Taken (OK)
Definitely not taken
Assume vector length = 100

## Slide 47: Avoiding Branches
On Modern Processor, Branches Very Expensive
  Unless prediction can be reliable
  When possible, best to avoid altogether
Example
  Compute maximum of two values
    14 cycles when prediction correct
    29 cycles when incorrect
int max(int x, int y)
{
return (x < y) ? y : x;
}
movl 12(%ebp),%edx # Get y
movl 8(%ebp),%eax # rval=x
cmpl %edx,%eax # rval:y
jge L11 # skip when >=
movl %edx,%eax # rval=y
L11:

## Slide 48: Conditional Move
  Added with P6 microarchitecture (PentiumPro onward)
  cmovXXl %edx, %eax
    If condition XX holds, copy %edx to %eax
    Doesn’t involve any branching – much more predictable
    Handled as operation within Execution Unit
movl 8(%ebp),%edx # Get x
movl 12(%ebp),%eax # rval=y
cmpl %edx, %eax # rval:x
cmovll %edx,%eax # If <, rval=x
  Current version of GCC won’t use this instruction
    Thinks it’s compiling for a 386
    Can turn on use of conditional move by gcc by compiling with optimization flags -O1, -O2, -O3, …
  Performance
    14 cycles on all data
Notes: For gcc flags and cmov, see for example https://gcc.gnu.org/onlinedocs/gcc/Optimize-Options.html

## Slide 49: Conditional Move
Writing code that is conditional-move-friendly
  For gcc, use conditional operations to compute outcome(s)
  Then assign the result variable(s)
  Example:
  1 /* Rearrange two vectors so that for each i, b[i] >= a[i] */
  2 void minmax2(int a[], int b[], int n) {
  3 int i;
  4 for (i = 0; i < n; i++) {
  5 int min = a[i] < b[i] ? a[i] : b[i];
  6 int max = a[i] < b[i] ? b[i] : a[i];
  7 a[i] = min;
  8 b[i] = max;
  9 }
  10}

## Slide 50: Limitations on Optimization
# Functional units of each type
  Don’t have unlimited resources
How deeply each operation can be pipelined
# registers => Register spilling
  If you over-parallelize, there are not enough data registers to hold all the accumulators, so they have to be stored in memory
Branch prediction
  must refill pipeline after a misprediction
Data dependencies in your graph
  a) slow down pipeline
  b) memory dependencies (next)
Amdahl’s Law (next)
Notes: Can also be limited the # functional units, and how deeply pipelined each functional unit can be.

## Slide 51: Memory Load/Store Bottlenecks (5.12)
x86 supports one Load unit and one Store unit to interact with memory
Load and Store functional units can initiate one load or store each clock cycle
  Latency is 3-4 clock cycles, so can pipeline 3-4 load or store instructions on each unit
Usually, can pipeline loads and stores, except
  A load can depend on a previous load, e.g. ls = ls->next
    i.e. the second load cannot begin until the first load has finished
  Loads can depend on previous stores to the same memory address, forming a write/read dependency
    i.e. if you write then read from the same memory location, must wait for write to complete before reading
Notes: Just as a data dependency on combine4 products (can’t do next multiply until previous multiply completes, because the next multiply depends on/needs the input from the results of the previous multiply) prevented us from taking advantage of pipelining multiplies, a similar data dependency prevents pipelining loads/stores.

## Slide 52: A Load Can Depend on a Prior Load
Example (64 bit):
# len in %eax, ls in %rdi
.L11: # loop:
addl $1, %eax # Increment len
movq (%rdi), %rdi # ls = ls->next
testq %rdi, %rdi # Test ls
jne .L11 # If nonnull, goto loop
Notes: The movq can be broken down into a load (%rdi) and a movq “load_result”, %rdi. As we iterate the loop, we execute the next load. But it cannot begin until the prior load has completed and updated %rdi.

## Slide 53: A Load Can Depend on a Prior Store
Example:
# what if %ecx = %ebx?
movl %eax,(%ecx) # Store
movl (%ebx),%eax # Load
addl $1,%eax
subl $1,%edx
jne loop
# if %ecx = %ebx, then you’re reading from the same memory location that was just written – the read must wait for the write to complete
CPU creates a store buffer of addresses of stores. A load must check the store buffer to see if there is a dependency before loading

## Slide 54: (Chapter 5) Amdahl’s Law – Know Your Limits!
The speedup in your program via parallelization is fundamentally limited by the slowest sequential portion of your program
T = time to execute a program
P = % of program that can be sped up a factor S times
T
S
New time T’ = P* + (1-P)*T
1
1-P +
P
S
Total speedup = T/T’ =
Ex. P=70%, S=100, Total speedup = 1/(.3 +.007) = 3.25!
1
1-P
As S-> ∞, T/T’ ->

## Slide 55: Machine-Dependent Opt. Summary
Loop Unrolling
  Some compilers do this automatically
  Generally not as clever as what can achieve by hand
Exposing Instruction-Level Parallelism
  Very machine dependent
Warning:
  Benefits depend heavily on particular machine
  Best if performed by compiler
    But GCC on IA32/Linux is not very good
  Do only for performance-critical parts of code

## Slide 56: Important Profiling Tools
Find the bottleneck…
Measurement
  Accurately compute time taken by code
    Most modern machines have built in cycle counters
    Using them to get reliable measurements is tricky
  Profile procedure calling frequencies
    Unix tool gprof
  Analyze memory performance, e.g. leaks
    valgrind
Observation
  Generating assembly code
    Lets you see what optimizations compiler can make
    Understand capabilities/limitations of particular compiler

## Slide 57: Code Profiling Example
Task
  Count word frequencies in text document
  Produce sorted list of words from most frequent to least
Steps
  Convert strings to lowercase
  Apply hash function
  Each hash bucket is a linked list.
  Search list,
    If not found, insert in list
    If found, increment counter for word
  Sort results
Data Set
  Collected works of Shakespeare
  946,596 total words, 26,596 unique
  Initial implementation: 9.2 seconds
29,801 | the
27,529 | and
21,029 | I
20,957 | to
18,514 | of
15,370 | a
14010 | you
12,936 | my
11,722 | in
11,519 | that
  Shakespeare’s
  most frequent words
Notes: Could also count pairs of words, this is a 2-gram. Can count occurrences of a sequence of N words (N-grams) as well.

## Slide 58: Hash Function
Takes a set of input values and maps/groups them into N subsets or buckets
Typically used to quickly classify/separate inputs into one of N possible categories
Example 1: if set of input values = all English words, then h(word) could classify a word by its first letter, creating 26 buckets, e.g. bucket ‘a’ contains all words starting with ‘a’…
Example 2: if set of input values = all integers, then h(num) = num mod 4 would classify the input into one of 4 buckets
N buckets:
Note the length of each
bucket denotes the #
of items hashed to that
bucket. For some but not
all hashes, a desired
property is that the hash
uniformly distributes the
input values to the buckets
Hash h(input)

## Slide 59: Code Profiling Example (cont.)
Task
  Count word frequencies in text document
  Produce sorted list of words from most frequent to least
Convert strings to lowercase
Shakespeare
words
count=1007
count=33
you
count=86
to
count=3105
the
count=4227
and
my
count=1
of
sort
Sorted
list
hash
Let hash = sum of letters in a word

## Slide 60: Code Profiling
Augment Executable Program with Timing Functions
  Computes (approximate) amount of time spent in each function
  Time computation method
    Periodically (~ every 10ms) interrupt program
    Determine what function is currently executing
    Increment its timer by interval (e.g., 10ms)
  Also maintains counter for each function indicating number of times called
Using
  gcc –O2 –pg prog.c –o prog
  ./prog
    Executes in normal fashion, but also generates file gmon.out
  gprof prog
    Generates profile information based on gmon.out

## Slide 61: Profiling Results
Call Statistics
  Number of calls and cumulative time for each function
Performance Limiter
  Using inefficient sorting algorithm
  Single call uses 87% of CPU time
% cumulative self self total
time seconds seconds calls ms/call ms/call name
86.60 8.21 8.21 1 8210.00 8210.00 sort_words
5.80 8.76 0.55 946596 0.00 0.00 lower1
4.75 9.21 0.45 946596 0.00 0.00 find_ele_rec
1.27 9.33 0.12 946596 0.00 0.00 h_add
Notes: The “cumulative seconds” field represents the total in this function *and* all of the functions above it in the table.
The “self seconds” field represents just the time in this function.

## Slide 62: Code Optimizations
  First step: Use more efficient sorting function
  Library function qsort
Notes: Note: the Sort time has all but disappeared. The textbook has a similar result: the Quicksort causes the sorting time to become less than 1% of the initial time.
Quicksort usually has O(n*log n) complexity.

## Slide 63: Further Optimizations
  Iter first: Use iterative function to insert elements into linked list
    Causes code to slow down
  Iter last: Iterative function, places new entry at end of list
    Tend to place most common words at front of list
  Big table: Increase number of hash buckets
  Better hash: spreads hash results more uniformly across buckets, thus reducing length of linked lists
  Linear lower: Move strlen out of loop
Notes: Note:

## Slide 64: Profiling Observations
Benefits
  Helps identify performance bottlenecks
  Especially useful when have complex system with many components
Limitations
  Only shows performance for data tested
  Timing mechanism fairly crude
    Only works for programs that run for > 3 seconds
  e.g., linear lower did not show big gain, since words are short
    Quadratic inefficiency could remain lurking in code, i.e. it could be revealed when input data is mostly longer word strings

## Slide 65: Role of Programmer
  How should I write my programs, given that I have a good, optimizing compiler?
Don’t: Completely Sacrifice Modularity for Performance
  Hard to read, maintain, & assure correctness
Do: Balance Modularity and Performance
  Write code that’s readable & maintainable
    Procedures, recursion, without built-in constant limits
    Even though these factors can slow down code
  Use profilers to identify bottlenecks
  Select best algorithm, e.g. best sorting algorithm
  Eliminate optimization blockers
    Allows compiler to do its job. And use optimization flags -O1, -O2,…
Focus on Inner Loops
  Do detailed optimizations where code will be executed repeatedly
  Will get most performance gain here

## Slide 66: Supplementary Slides

## Slide 67: Compiler-Generated Code Motion (-O1)
set_row:
testq %rcx, %rcx # Test n
jle .L1 # If 0, goto done
imulq %rcx, %rdx # ni = n*i
leaq (%rdi,%rdx,8), %rdx # rowp = A + ni*8
movl $0, %eax # j = 0
.L3: # loop:
movsd (%rsi,%rax,8), %xmm0 # t = b[j]
movsd %xmm0, (%rdx,%rax,8) # M[A+ni*8 + j*8] = t
addq $1, %rax # j++
cmpq %rcx, %rax # j:n
jne .L3 # if !=, goto loop
.L1: # done:
rep ; ret
long j;
long ni = n*i;
double *rowp = a+ni;
for (j = 0; j < n; j++)
*rowp++ = b[j];
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}

## Slide 68: Calling Strlen
Strlen performance
  Only way to determine length of string is to scan its entire length, looking for null character.
Overall performance, string of length N
  N calls to strlen
  Require times N, N-1, N-2, …, 1
  Overall O(N2) performance
/* My version of strlen */
size_t strlen(const char *s)
{
size_t length = 0;
while (*s != '\0') {
s++;
length++;
}
return length;
}

## Slide 69: Memory Matters
  Code updates b[i] on every iteration
  Why couldn’t compiler optimize this away?
# sum_rows1 inner loop
.L4:
movsd (%rsi,%rax,8), %xmm0 # FP load
addsd (%rdi), %xmm0 # FP add
movsd %xmm0, (%rsi,%rax,8) # FP store
addq $8, %rdi
cmpq %rcx, %rdi
jne .L4
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}

## Slide 70: Memory Aliasing
  Code updates b[i] on every iteration
  Must consider possibility that these updates will affect program behavior
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}
double A[9] =
{ 0, 1, 2,
4, 8, 16,
32, 64, 128};
double B[3] = A+3;
sum_rows1(A, B, 3);
i = 0: [3, 8, 16]
init: [4, 8, 16]
i = 1: [3, 22, 16]
i = 2: [3, 22, 224]
Value of B:

## Slide 71: Removing Aliasing
  No need to store intermediate results
# sum_rows2 inner loop
.L10:
addsd (%rdi), %xmm0 # FP load + add
addq $8, %rdi
cmpq %rax, %rdi
jne .L10
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows2(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
double val = 0;
for (j = 0; j < n; j++)
val += a[i*n + j];
b[i] = val;
}
}

## Slide 72: Optimization Blocker: Memory Aliasing
Aliasing
  Two different memory references specify single location
  Easy to have happen in C
    Since allowed to do address arithmetic
    Direct access to storage structures
  Get in habit of introducing local variables
    Accumulating within loops
    Your way of telling compiler not to check for aliasing

## Slide 73: Exploiting Instruction-Level Parallelism
Need general understanding of modern processor design
  Hardware can execute multiple instructions in parallel
Performance limited by data dependencies
Simple transformations can yield dramatic performance improvement
  Compilers often cannot make these transformations
  Lack of associativity and distributivity in floating-point arithmetic

## Slide 74: Benchmark Computation
Data Types
  Use different declarations for data_t
  int
  long
  float
  double
Operations
  Use different definitions of OP and IDENT
  + / 0
  * / 1
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements

## Slide 75: Benchmark Example: Data Type for Vectors
Data Types
  Use different declarations for data_t
  int
  long
  float
  double
/* data structure for vectors */
typedef struct{
size_t len;
data_t *data;
} vec;
/* retrieve vector element
and store at val */
int get_vec_element
(*vec v, size_t idx, data_t *val)
{
if (idx >= v->len)
return 0;
*val = v->data[idx];
return 1;
}
len
data
0
1
len-1

## Slide 76: Cycles Per Element (CPE)
Convenient way to express performance of program that operates on vectors or lists
Length = n
In our case: CPE = cycles per OP
T = CPE*n + Overhead
  CPE is slope of line
Chart: Elements
| 0.0 | 193.0 | 120.0 | 91.0 | 95.0 | 196.0 | 97.0 | 181.0 | 91.0 | 83.0 | 43.0 | 183.0 | 140.0 | 146.0 | 94.0 | 134.0 | 163.0 | 131.0 | 110.0 | 182.0 | 189.0 | 112.0 | 141.0 | 185.0 | 188.0 | 47.0 | 130.0 | 102.0 | 59.0 | 174.0
psum1 | 2112.6 | 1451.1 | 1188.6 | 1218 | 2131.5 | 1247.4 | 2003.4 | 1190.7 | 1117.2 | 758.1 | 2020.2 | 1629.6 | 1686.3 | 1211.7 | 1568.7 | 1841.7 | 1543.5 | 1358.7 | 2011.8 | 2066.4 | 1373.4 | 1635.9 | 2032.8 | 2058 | 787.5 | 1539.3 | 1285.2 | 905.1 | 1938.3
psum1i | 367.79 | 2107.43 | 1449.43 | 1188.03 | 1224.09 | 2134.47 | 1242.12 | 1999.27 | 1188.03 | 1115.92 | 755.38 | 2017.29 | 1629.7 | 1683.79 | 1215.07 | 1575.62 | 1837.02 | 1548.58 | 1359.29 | 2008.28 | 2071.37 | 1377.32 | 1638.72 | 2035.32 | 2062.36 | 791.43 | 1539.57 | 1287.18 | 899.6 | 1936.17
psum2 | 1535.1 | 1100.4 | 921.9 | 940.8 | 1545.6 | 949.2 | 1455.3 | 917.7 | 865.2 | 623.7 | 1467.9 | 1209.6 | 1253.7 | 936.6 | 1173.9 | 1352.4 | 1150.8 | 1029 | 1461.6 | 1509.9 | 1039.5 | 1215.9 | 1478.4 | 1505.7 | 642.6 | 1152.9 | 987 | 732.9 | 1419.6
psum2i | 367.66 | 1531.11 | 1091.05 | 916.23 | 940.34 | 1549.2 | 952.4 | 1458.77 | 916.23 | 868.01 | 626.87 | 1470.83 | 1211.62 | 1247.79 | 934.32 | 1175.45 | 1350.27 | 1157.36 | 1030.77 | 1464.8 | 1507 | 1042.82 | 1217.64 | 1482.89 | 1500.97 | 650.99 | 1151.33 | 982.54 | 723.33 | 1416.58
psum1
Slope = 9.0
psum2
Slope = 6.0

## Slide 77: Benchmark Performance
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 unoptimized | 22.68 | 20.02 | 19.98 | 20.18
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14

## Slide 78: Basic Optimizations
Move vec_length out of loop
Avoid bounds check on each cycle
Accumulate in temporary
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}

## Slide 79: Effect of Basic Optimizations
Eliminates sources of overhead in loop
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14
Combine4 | 1.27 | 3.01 | 3.01 | 5.01

## Slide 80: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 81: Superscalar Processor
Definition: A superscalar processor can issue and execute multiple instructions in one cycle. The instructions are retrieved from a sequential instruction stream and are usually scheduled dynamically.
Benefit: without programming effort, superscalar processor can take advantage of the instruction level parallelism that most programs have
Most modern CPUs are superscalar.
Intel: since Pentium (1993)

## Slide 82: Pipelined Functional Units
  Divide computation into stages
  Pass partial computations from stage to stage
  Stage i can start on new computation once values passed to i+1
  E.g., complete 3 multiplications in 7 cycles, even though each requires 3 cycles
Stage 1
Stage 2
Stage 3
long mult_eg(long a, long b, long c) {
long p1 = a*b; long p2 = a*c; long p3 = p1 * p2;
return p3; }
 | Time |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stage 1 | a*b | a*c |  |  | p1*p2 |  | 
Stage 2 |  | a*b | a*c |  |  | p1*p2 | 
Stage 3 |  |  | a*b | a*c |  |  | p1*p2

## Slide 83: Haswell CPU
  8 Total Functional Units
Multiple instructions can execute in parallel
  2 load, with address computation
  1 store, with address computation
  4 integer
  2 FP multiply
  1 FP add
  1 FP divide
Some instructions take > 1 cycle, but can be pipelined
  Instruction Latency Cycles/Issue
  Load / Store 4 1
  Integer Multiply 3 1
  Integer/Long Divide 3-30 3-30
  Single/Double FP Multiply 5 1
  Single/Double FP Add 3 1
  Single/Double FP Divide 3-15 3-15

## Slide 84: x86-64 Compilation of Combine4
Inner Loop (Case: Integer Multiply)
.L519: # Loop:
imull (%rax,%rdx,4), %ecx # t = t * d[i]
addq $1, %rdx # i++
cmpq %rdx, %rbp # Compare length:i
jg .L519 # If >, goto Loop
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 85: Combine4 = Serial Computation (OP = *)
Computation (length=8)
  ((((((((1 * d[0]) * d[1]) * d[2]) * d[3]) * d[4]) * d[5]) * d[6]) * d[7])
Sequential dependence
  Performance: determined by latency of OP
*
*
1
d0
d1
*
d2
*
d3
*
d4
*
d5
*
d6
*
d7

## Slide 86: Loop Unrolling (2x1)
Perform 2x more useful work per iteration
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = (x OP d[i]) OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}

## Slide 87: Effect of Loop Unrolling
Helps integer add
  Achieves latency bound
Others don’t improve. Why?
  Still sequential dependency
x = (x OP d[i]) OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 88: Loop Unrolling with Reassociation (2x1a)
Can this change the result of the computation?
Yes, for FP. Why?
void unroll2aa_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = x OP (d[i] OP d[i+1]);
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}
x = (x OP d[i]) OP d[i+1];
Compare to before

## Slide 89: Effect of Reassociation
Nearly 2x speedup for Int *, FP +, FP *
  Reason: Breaks sequential dependency
  Why is that? (next slide)
x = x OP (d[i] OP d[i+1]);
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
2 func. units for FP *
2 func. units for load
4 func. units for int +
2 func. units for load

## Slide 90: Reassociated Computation
What changed:
  Ops in the next iteration can be started early (no dependency)
Overall Performance
  N elements, D cycles latency/op
  (N/2+1)*D cycles: CPE = D/2
*
*
1
*
*
*
d1
d0
*
d3
d2
*
d5
d4
*
d7
d6
x = x OP (d[i] OP d[i+1]);

## Slide 91: Loop Unrolling with Separate Accumulators (2x2)
Different form of reassociation
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x0 = IDENT;
data_t x1 = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x0 = x0 OP d[i];
}
*dest = x0 OP x1;
}

## Slide 92: Effect of Separate Accumulators
Int + makes use of two load units
2x speedup (over unroll2) for Int *, FP +, FP *
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Unroll 2x2 | 0.81 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 93: Separate Accumulators
*
*
1
d1
d3
*
d5
*
d7
*
*
*
1
d0
d2
*
d4
*
d6
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
What changed:
  Two independent “streams” of operations
Overall Performance
  N elements, D cycles latency/op
  Should be (N/2+1)*D cycles: CPE = D/2
  CPE matches prediction!
What Now?

## Slide 94: Unrolling & Accumulating
Idea
  Can unroll to any degree L
  Can accumulate K results in parallel
  L must be multiple of K
Limitations
  Diminishing returns
    Cannot go beyond throughput limitations of execution units
  Large overhead for short lengths
    Finish off iterations sequentially

## Slide 95: Unrolling & Accumulating: Double *
Case
  Intel Haswell
  Double FP Multiplication
  Latency bound: 5.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 
2 |  | 2.51 |  | 2.51 |  | 2.51 |  | 
3 |  |  | 1.67 |  |  |  |  | 
4 |  |  |  | 1.25 |  | 1.26 |  | 
6 |  |  |  |  | 0.84 |  |  | 0.88
8 |  |  |  |  |  | 0.63 |  | 
10 |  |  |  |  |  |  | 0.51 | 
12 |  |  |  |  |  |  |  | 0.52
Accumulators

## Slide 96: Unrolling & Accumulating: Int +
Case
  Intel Haswell
  Integer addition
  Latency bound: 1.00. Throughput bound: 1.00
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 1.27 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 
2 |  | 0.81 |  | 0.69 |  | 0.54 |  | 
3 |  |  | 0.74 |  |  |  |  | 
4 |  |  |  | 0.69 |  | 1.24 |  | 
6 |  |  |  |  | 0.56 |  |  | 0.56
8 |  |  |  |  |  | 0.54 |  | 
10 |  |  |  |  |  |  | 0.54 | 
12 |  |  |  |  |  |  |  | 0.56
Accumulators

## Slide 97: Achievable Performance
Limited only by throughput of functional units
Up to 42X improvement over original, unoptimized code
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Best | 0.54 | 1.01 | 1.01 | 0.52
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 98: Getting High Performance
Good compiler and flags
Watch out for hidden algorithmic inefficiencies
Write compiler-friendly code
  Watch out for optimization blockers: procedure calls & memory references
Look carefully at innermost loops (where most work is done)

## Slide 99: Time Scales
Absolute Time
  Typically use nanoseconds
    10–9 seconds
  Time scale of computer instructions
Clock Cycles
  Most computers controlled by high frequency clock signal
  Typical Range
    100 MHz
      108 cycles per second
      Clock period = 10ns
    2 GHz
      2 X 109 cycles per second
      Clock period = 0.5ns

## Slide 100: Lower Case Conversion Performance
  Time doubles when double string length
  Linear performance

## Slide 101: Recap…
Improving software performance
void combine1(vec_ptr v, int *dest)
{
int i;
*dest = 0;
for (i = 0; i < vec_length(v); i++) {
int val;
get_vec_element(v, i, &val);
*dest += val;
}
}
combine2
combine3
combine4
Machine-independent optimizations
void combine4(vec_ptr v,
int *dest)
{
int i;
int length = vec_length(v);
int *data = get_vec_start(v);
int sum = 0;
for (i = 0; i < length; i++)
sum += data[i];
*dest = sum;
}
How does combine4 achieves a CPE of 2 ?
  Need low level assembly
  How is it mapped to 2 x86 integer functional units?
load (%eax,%edx.0,4)  t.1
iaddl t.1, %ecx.0  %ecx.1
incl %edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1

## Slide 102: Combine4 Sum over 2 Integer Units
Performance
  Delay = 4-5 cycles, but CPE = 2.0
Time
cc.1
t.1
%ecx.i +1
incl
cmpl
jl
load
%edx.0
%edx.1
%ecx.0
addl
%ecx.1
load

## Slide 103: Recap…
Improving software performance
Can we achieve a CPE below 2?
combine5 unrolls loop and gets CPE ≈ 1, machine-dependent
combine5...{
...
for (i = 0; i < limit; i+=3) {
sum += data[i] + data[i+1]
+ data[i+2];
}
...
}

## Slide 104: Recap…
combine6 uses *both* loop unrolling *and* parallel independent accumulators
combine6...{
...
for (i = 0; i < limit; i+=3) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+1];
acc2 = acc2 + data[i+2];
}
sum = acc0 + acc1 + acc2;
...
}
Loop unrolling with k=3, and
Parallel accumulators
Doesn’t help much for addition, but it does help a lot for multiplication
...
for (i = 0; i < limit; i++) {
x *= data[i];
}
...
*dest = x;
Before Optimization:
Before Optimization, CPE = 4
cc.1
t.1
load
%ecx.1
incl
cmpl
jl
%edx.0
%edx.1
%ecx.0
imull
Time

## Slide 105: Loop Unrolling + Parallel Products
Can keep 4-cycle multiplier busy by pipelining two multiplications
After optimization: CPE = 2.0 !
...
for (i = 0; i < limit; i+=2) {
x0 *= data[i];
x1 *= data[i+1];
}
...
*dest = x0 * x1;

## Slide 106: Great Reality #4
There’s more to performance than asymptotic complexity
Constant factors matter too!
  Easily see 10:1 performance range depending on how code is written
  Must optimize at multiple levels:
    algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs are compiled and executed
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 107: Translation Example
Version of Combine4
  Integer data, multiply operation
Translation of First Iteration
.L24: # Loop:
imull (%eax,%edx,4),%ecx # t *= data[i]
incl %edx # i++
cmpl %esi,%edx # i:length
jl .L24 # if < goto Loop
.L24:
imull (%eax,%edx,4),%ecx
incl %edx
cmpl %esi,%edx
jl .L24
load (%eax,%edx.0,4)  t.1
imull t.1, %ecx.0  %ecx.1
incl %edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1

## Slide 108: Translation Example #1
  Split into two operations
    load reads from memory to generate temporary result t.1
    Multiply operation just operates on registers
  Operands
    Registers %eax does not change in loop. Values will be retrieved from register file during decoding
    Register %ecx changes on every iteration. Uniquely identify different versions as %ecx.0, %ecx.1, %ecx.2, …
      Register renaming
      Values passed directly from producer to consumers
imull (%eax,%edx,4),%ecx
load (%eax,%edx.0,4)  t.1
imull t.1, %ecx.0  %ecx.1

## Slide 109: Translation Example #2
  Register %edx changes on each iteration. Rename as %edx.0, %edx.1, %edx.2, …
incl %edx
incl %edx.0  %edx.1

## Slide 110: Translation Example #3
  Condition codes are treated similar to registers
  Assign tag to define connection between producer and consumer
cmpl %esi,%edx
cmpl %esi, %edx.1  cc.1

## Slide 111: Translation Example #4
  Instruction control unit determines destination of jump
  Predicts whether will be taken and target
  Starts fetching instruction at predicted destination
  Execution unit simply checks whether or not prediction was OK
  If not, it signals instruction control
    Instruction control then “invalidates” any operations generated from misfetched instructions
    Begins fetching and decoding instructions at correct target
jl .L24
jl-taken cc.1

## Slide 112: Results for Alpha Processor
  Overall trends very similar to those for Pentium III.
  Even though very different architecture and compiler

## Slide 113: Results for Pentium 4
  Higher latencies (int * = 14, fp + = 5.0, fp * = 7.0)
    Clock runs at 2.0 GHz
    Not an improvement over 1.0 GHz P3 for integer *
  Avoids FP multiplication anomaly

## Slide 114: Avoiding Branches with Bit Tricks
  In style of Lab #1
  Use masking rather than conditionals
  Compiler still uses conditional
    16 cycles when predict correctly
    32 cycles when mispredict
int bmax(int x, int y)
{
int mask = -(x>y);
return (mask & x) | (~mask & y);
}
xorl %edx,%edx # mask = 0
movl 8(%ebp),%eax
movl 12(%ebp),%ecx
cmpl %ecx,%eax
jle L13 # skip if x<=y
movl $-1,%edx # mask = -1
L13:

## Slide 115: Avoiding Branches with Bit Tricks
  Force compiler to generate desired code
  volatile declaration forces value to be written to memory
    Compiler must therefore generate code to compute t
    Simplest way is setg/movzbl combination
  Not very elegant!
    A hack to get control over compiler
  22 clock cycles on all data
    Better than misprediction
int bvmax(int x, int y)
{
volatile int t = (x>y);
int mask = -t;
return (mask & x) |
(~mask & y);
}
movl 8(%ebp),%ecx # Get x
movl 12(%ebp),%edx # Get y
cmpl %edx,%ecx # x:y
setg %al # (x>y)
movzbl %al,%eax # Zero extend
movl %eax,-4(%ebp) # Save as t
movl -4(%ebp),%eax # Retrieve t